3DATA DESCRIPTION FOR FILE <Meteor60.csv>

CONTRIBUTORS

Toste Tanhua

Leibniz Institute of Marine Sciences at Kiel University
Marine Biogeochemistry 
Duesternbrooker Weg 20 
D-24105 Kiel, 
Germany 
Email: ttanhua@ifm-geomar.de

Douglas W.R. Wallace (CHIEF SCIENTIST)

Leibniz Institute of Marine Sciences at Kiel University
Marine Biogeochemistry 
Duesternbrooker Weg 20 
D-24105 Kiel, 
Germany 
Email: dwallace@ifm-geomar.de

SCOPE

Hydrographical and chemical data made during the German Meteor 60/5 cruise in the mid-latitude North Atlantic. Start of cruise:2004.0311. End of cruise: 2004.04.13

# DATA DESCRIPTION

The methods, corrections and post-cruise calibration procedures are described below.

CTD WORK

The temperature and salinity are reported on the ITS-90 and PSS-78 calibration scales, respectively. For more information regarding CTD data, contact Jens Schafstall (jschafstall@ifm-geomar.de).

| Instrument Type | SBE 11 plus | Serial No. |
| --- | --- | --- |
| CTD deck unit | SBE 9plus |  |
| CTD underwater unit | SBE 32 | 09P22348-0572 |
| Rosette water sampler | SBE 3plus | 3222348-0291 |
| Temperature sensor | 4c | 03P2920 |
| Conductivity sensor | SBE | 042443 |
| Oxygen sensor | SBE 43 | 430214 |
| Pump | SBE 5T | 052603 |
| Pinger | Benthos |  |
| Bottom alarm | mechanic switch |  |

Bottle salinity were measured on a Guildline Autosal 8 salinometer. The precision between replicate measurements were 0.003 units.

TOTAL ALKALINITY

Potentiometric titration [Mintrop et al., 2000].

CRM corrected from 4 separate batches (batch # 58, 60, 63 and 64). The mean difference between measurements and the Certified values was -1.19 ( 0.69 (mol kg-1 (95% confidence interval, n=69). Alkalinity values have been adjusted to the certified value by addition of this mean offset. Precision of the total alkalinity single measurement was 4.28 (mol kg-1 (95% confidence interval), determined from measurements of duplicate samples.

Based on cross over with contemporary CLIVAR cruises and with TTO/NAS, we suggest that the total alkalinity is corrected by adding 1.6 umol/kg from the original data (not applied to the submitted data).

The background and procedures of the correction is described in detail by Tanhua and

Wallace (2005).

DISSOLVED INORGANIC CARBON (DIC)

Coulometric titration [Johnson et al., 1993].

CRM corrected from 4 separate batches (batch # 58, 60, 63 and 64). Mean offset between our measurements and the Certified Values was 1.02 ( 0.44 (mol kg-1 (95% confidence interval, n = 88). Measured DIC concentrations were therefore adjusted to the manometric Certified calibration scale by subtraction of this mean offset. Precision of the measurements was 1.49 (mol kg-1 (95% confidence interval), as determined from analyses of duplicate samples.

The background and procedures of the correction is described in detail by Tanhua and

Wallace [2005].

OXYGEN

Oxygen measurements performed by Frank Malien (fmalien@ifm-geomar.de) by means of Winkler titration. The precision estimated from double samples (95 % confidence interval) is estimated to ( 0.55 (mol/kg.

NUTRIENTS

Nutrient analysis performed by Frank Malien (fmalien@ifm-geomar.de).

The following precision was calculated for the nutrient data (95% confidence);

NO3 ( 0.18 (mol/kg and SIO2 ( 0.19 (mol/kg, calculated from measurements of double samples.

The nutrient data was compared with crossover stations for contemporary CLIVAR lines (A16, A22 and A20). Based on these cross over stations, we suggest the following corrections to the nutrient data (not applied to the submitted data).

M60 Silicate values too low in the high concentration range compared to CLIVAR data, therefore we suggest the following corrections;

For Si<20 (mol/kg;  Si(corr)=Si

For 20<Si<30 (mol/kg; Si(corr)=Si+(Si-20)*0.2

For Si>30 (mol/kg; Si(corr)=Si+2

M60 nitrate values are low in the high concentration range compared to CLIVAR data, therefore we suggest the following corrections;

NO3<10 (mol/kg;  NO3(corr)=NO3

NO3>10 (mol/kg;  NO3(corr)=NO3+(NO3-10)*0.05

The PO4 data from M60/5 was subject to some analytical difficulties and were of noticeably poorer quality than the other parameters, and are flagged accordingly.

CFCs

The CFC measurements performed during M60/5 were made on an analytical system similar to that described by Bullister and Weiss and are reported on the SIO98 scale. The analytical precision was determined to be 0.7 and 0.6 % for CFC-12, CFC-11, respectively, as calculated from duplicate samples, typically at two depths per station.

We determined a sampling blank of 0.007, 0.010 and 0.045 pmol/kg for CFC-12, CFC-11 and CCl4, respectively, determined as the median value of 18 deep water samples in the eastern basin. The data has been corrected for this sampling blank.

DATA FORMAT

The data are supplied in comma separated format (.csv).

The header records;

Sample ID, Station#, Cast #, Pressure (dbar), Day, Month , Year, Lat (°N), Lon (°E), Temperature (ITS-90), Salinity (PS-78), CFC-12 (pmol/kg), CFC-11 (pmol/kg), CCl4 (pmol/kg), Oxygen (umol/kg), SiO4 (umol/kg), PO4 (umol/kg), NO3 (umol/kg), NO2 (umol/kg), DIC-calc (umol/kg), Total Alkalinity (umol/kg).

Missing data are denoted with –999, the units for the revised data are identical with the

original data.

OTHER MESUREMENTS

SF6 and CH3CCl3; Contact Toste Tanhua (ttanhua@ifm-geomar.de).

N2O; Contact Hermann Bange (hbange@ifm-geomar.de)

Carbon isotopes; Contact Douglas Wallace (dwallace@ifm-geomar.de)

Bioincubations; Contact Matt Mills (mmills@ifm-geomar.de)

Iron speciation; Contact Eric Achterberg (eric@noc.soton.ac.uk)

Brominated organohalgens; Contact Douglas Wallase (dwallace@ifm-geomar.de).

REFERENCES

Bullister, J.L. and Weiss, R.F., 1988. Determination of CCl3F and CCl2F2 in seawater and air. Deep-Sea Research, 35(5): 839-853.

Mintrop, L., F.F. Perez, M. Gonzalez-Davila, J.M. Santana-Casiano, and A. Körtzinger (2000), Alkalintiy determination by potentiometri: intercalibration using three different methods, Scienc. Mar., 26, 1, 23-37.

Johnson, K., K.D. Willis, D.B. Butler, W.K. Johnson, and C.S. Wong (1993), Coulometric carbon dioxide analysis for marine studies: Maximizing the performance of an automated gas extraction system and coulometric detector, Mar. Chem., 44 (2-4), 167-188.

Tanhua, T., and D.W.R. Wallace (2005), Consistency of TTO-NAS Inorganic Carbon Data with modern measurements, Geophys. Res. Lett., 32, L14618, doi:10.1029/2005GL032348.