- Cruise narrative

- Highlights

Cruise designation: RF15-07 (WHP-P04W revisit)

- EXPOCODE: 49UP20150724

- Chief scientist: Keizo SHUTTA (shutta.kei@met.kishou.go.jp)

Marine Division

Global Environment and Marine Department

Japan Meteorological Agency (JMA)

1-3-4, Otemachi, Chiyoda-ku, Tokyo 100-8122, JAPAN

Phone: +81-3-3212-8341 Ext. 4763

- Ship name: R/V Ryofu Maru

- Ports of call: Leg 1: Tokyo – Pohnpei, Leg 2: Pohnpei–Tokyo

- Cruise dates: Leg 1: 24 July 2015–18 August 2015
Leg 2: 22 August 2015–15 September 2015

- Floats and drifters deployed: 2 Floats

- Cruise Summary Information

RF15-07 cruise was carried out during the period from July 24 to September 15, 2015. The cruise started from Japan, and sailed towards south east to the first station. Hydrographic observation started near Marshal Islands followed by sailing towards west along latitude approximately 10°N. This line was observed by Woods Hole Oceanographic Institution in 1989 as ‘WHP-P04’, which is a part of WOCE (World Ocean Circulation Experiment) Hydrographic Programme.

A total of 66 stations was occupied using a Sea-Bird Electronics (SBE) 36 position carousel equipped with 10-liter Niskin water sample bottles, a CTD system (SBE911plus) equipped with SBE35 deep ocean standards thermometer, JFE Advantech oxygen sensor (RINKO III), Teledyne Benthos altimeter (PSA-916D), and Teledyne RD Instruments L-ADCP (300kHz). To examine consistency of data, we carried out the observation twice at 9°30’N, 162°30’E (Stn.35 and 36). Cruise track and station location are shown in Figure 1.

At each station, full-depth CTDO2 (temperature, conductivity (salinity) and dissolved oxygen) profile and up to 36 water samples were taken and analyzed. Water samples were obtained from 10 dbar to approximately 10 m above the bottom. In addition, surface water was sampled using a stainless steel bucket at each station. Sampling layer is designed as so-called staggered mesh as shown in Table 1 (Swift, 2010). The bottle depth diagram is shown in Figure 2.

Water samples were analyzed for salinity, dissolved oxygen, nutrients, dissolved inorganic carbon (DIC), total alkalinity (TA), pH, CFC-11, CFC-12 and phytopigment (chlorophyll-a and phaeopigments). Underway measurements of partial pressure of carbon dioxide (pCO2), temperature, salinity, chlorophyll-a, subsurface current, bathymetry and meteorological parameters were conducted along the cruise track.

R/V Ryofu Maru departed Tokyo (Japan) on July 24, 2015. Before the observation at the first station, all watch standers were drilled in the method of sample drawing and CTD operations near Izu-Oshima (34°42’N, 139°51’E). The hydrographic cast of CTDO2 was started at the first station (Stn.66 (9°30’N, 178°48’E; RF5486)) on August 2, 2015. Leg 1 consisted of 31 stations from Stn.66 to Stn.36 (9°30’N, 162°31’E; RF5516). She called for Pohnpei (Federated States of Micronesia) on August, 18 (Leg 1). She left Pohnpei on August 22, 2015 for Tokyo (Japan) and arrived on September 15, 2015 (Leg 2). Leg 2 consisted of 35 stations from Stn.35 (9°29’N, 162°29’E; RF5517) to Stn.1 (9°N, 137°E; RF5551). Location data of stations is shown in Table 2.

Two Argo floats were deployed along the cruise track. The information of deployed the floats are listed in Table 3.

Figure 1. Cruise track of RF15-07.

Figure 2. The bottle depth diagram for WHP-P04 revisit.

Table 1. The scheme of sampling layer in meters.

|  | 9゜N (Stn.1 - Stn.66) |  |  | 9゜N (Stn.1 - Stn.66) |
| --- | --- | --- | --- | --- |
| Bottle count | Scheme1 | Scheme2 | Scheme3 |  | Bottle count | Scheme1 | Scheme2 | Scheme3 |
| 1 | 10 | 10 | 10 |  | 21 | 1600 | 1670 | 1530 |
| 2 | 25 | 25 | 25 |  | 22 | 1800 | 1870 | 1730 |
| 3 | 50 | 50 | 50 |  | 23 | 2000 | 2070 | 1930 |
| 4 | 75 | 75 | 75 |  | 24 | 2200 | 2270 | 2130 |
| 5 | 100 | 100 | 100 |  | 25 | 2400 | 2470 | 2330 |
| 6 | 125 | 125 | 125 |  | 26 | 2600 | 2670 | 2530 |
| 7 | 150 | 150 | 150 |  | 27 | 2800 | 2870 | 2730 |
| 8 | 175 | 175 | 175 |  | 28 | 3000 | 3080 | 2930 |
| 9 | 200 | 200 | 200 |  | 29 | 3250 | 3330 | 3170 |
| 10 | 250 | 250 | 250 |  | 30 | 3500 | 3580 | 3420 |
| 11 | 300 | 330 | 280 |  | 31 | 3750 | 3830 | 3670 |
| 12 | 400 | 430 | 370 |  | 32 | 4000 | 4080 | 3920 |
| 13 | 500 | 530 | 470 |  | 33 | 4250 | 4330 | 4170 |
| 14 | 600 | 630 | 570 |  | 34 | 4500 | 4580 | 4420 |
| 15 | 700 | 730 | 670 |  | 35 | 4750 | 4830 | 4670 |
| 16 | 800 | 830 | 770 |  | 36 | 5000 | 5080 | 4920 |
| 17 | 900 | 930 | 870 |  | 37 | 5250 | 5330 | 5170 |
| 18 | 1000 | 1070 | 970 |  | 38 | 5500 | 5580 | 5420 |
| 19 | 1200 | 1270 | 1130 |  | 39 | 5750 | 5830 | 5670 |
| 20 | 1400 | 1470 | 1330 |  | 40 | 6000 | 6000 | 6000 |

Table 2. Station data of RF15-07 cruise. The ‘RF’ column indicates the JMA station identification number.

| Leg | Station | Position |  | Leg | Station | Position |
| --- | --- | --- | --- | --- | --- | --- |
|  | Stn. | RF | Latitude | Longitude |  |  | Stn. | RF | Latitude | Longitude |
| 2 | 1 | 5551 | 8-59.51 N | 136-59.79 E |  | 1 | 36 | 5516 | 9-30.02 N | 162-30.74 E |
| 2 | 2 | 5550 | 9-00.35 N | 137-49.10 E |  | 1 | 37 | 5515 | 9-29.80 N | 163-20.14 E |
| 2 | 3 | 5549 | 8-59.33 N | 138-11.38 E |  | 1 | 38 | 5514 | 10-01.06 N | 164-01.07 E |
| 2 | 4 | 5548 | 8-59.23 N | 138-41.11 E |  | 1 | 39 | 5513 | 9-30.66 N | 163-59.35 E |
| 2 | 5 | 5547 | 8-59.36 N | 139-35.34 E |  | 1 | 40 | 5512 | 9-01.16 N | 163-59.54 E |
| 2 | 6 | 5546 | 9-04.38 N | 140-23.73 E |  | 1 | 41 | 5511 | 7-59.93 N | 163-58.52 E |
| 2 | 7 | 5545 | 9-07.51 N | 141-13.56 E |  | 1 | 42 | 5510 | 7-00.40 N | 164-29.95 E |
| 2 | 8 | 5544 | 9-14.43 N | 142-12.20 E |  | 1 | 43 | 5509 | 6-01.10 N | 165-00.94 E |
| 2 | 9 | 5543 | 9-17.02 N | 142-51.00 E |  | 1 | 44 | 5508 | 5-01.27 N | 165-05.64 E |
| 2 | 10 | 5542 | 9-22.65 N | 143-42.11 E |  | 1 | 45 | 5507 | 5-00.67 N | 165-40.86 E |
| 2 | 11 | 5541 | 9-27.78 N | 144-30.22 E |  | 1 | 46 | 5506 | 5-00.86 N | 166-20.43 E |
| 2 | 12 | 5540 | 9-35.18 N | 145-19.27 E |  | 1 | 47 | 5505 | 5-00.73 N | 167-01.30 E |
| 2 | 13 | 5539 | 9-31.20 N | 145-50.19 E |  | 1 | 48 | 5504 | 5-00.53 N | 167-41.10 E |
| 2 | 14 | 5538 | 9-31.00 N | 146-19.11 E |  | 1 | 49 | 5503 | 5-00.01 N | 168-20.87 E |
| 2 | 15 | 5537 | 9-30.88 N | 147-00.57 E |  | 1 | 50 | 5502 | 5-01.17 N | 169-00.67 E |
| 2 | 16 | 5536 | 9-30.48 N | 147-37.58 E |  | 1 | 51 | 5501 | 5-00.69 N | 169-30.60 E |
| 2 | 17 | 5535 | 9-35.25 N | 148-05.82 E |  | 1 | 52 | 5500 | 4-59.45 N | 170-00.27 E |
| 2 | 18 | 5534 | 9-30.33 N | 148-45.85 E |  | 1 | 53 | 5499 | 5-00.96 N | 170-40.84 E |
| 2 | 19 | 5533 | 9-33.77 N | 149-20.78 E |  | 1 | 54 | 5498 | 5-00.84 N | 171-20.15 E |
| 2 | 20 | 5532 | 9-31.01 N | 150-01.31 E |  | 1 | 55 | 5497 | 4-59.86 N | 172-00.93 E |
| 2 | 21 | 5531 | 9-30.61 N | 150-51.12 E |  | 1 | 56 | 5496 | 5-17.28 N | 172-31.21 E |
| 2 | 22 | 5530 | 9-30.80 N | 151-41.26 E |  | 1 | 57 | 5495 | 5-34.83 N | 173-00.08 E |
| 2 | 23 | 5529 | 9-30.04 N | 152-29.82 E |  | 1 | 58 | 5494 | 5-37.67 N | 173-30.23 E |
| 2 | 24 | 5528 | 9-29.59 N | 153-20.15 E |  | 1 | 59 | 5493 | 6-12.87 N | 174-10.65 E |
| 2 | 25 | 5527 | 9-29.59 N | 154-10.33 E |  | 1 | 60 | 5492 | 6-42.43 N | 175-00.03 E |
| 2 | 26 | 5526 | 9-29.81 N | 155-00.36 E |  | 1 | 61 | 5491 | 7-10.53 N | 175-49.42 E |
| 2 | 27 | 5525 | 9-29.74 N | 155-51.13 E |  | 1 | 62 | 5490 | 7-38.81 N | 176-39.10 E |
| 2 | 28 | 5524 | 9-30.69 N | 156-41.11 E |  | 1 | 63 | 5489 | 8-04.76 N | 177-29.13 E |
| 2 | 29 | 5523 | 9-30.28 N | 157-30.43 E |  | 1 | 64 | 5488 | 8-33.21 N | 178-19.33 E |
| 2 | 30 | 5522 | 9-29.44 N | 158-20.83 E |  | 1 | 65 | 5487 | 8-59.18 N | 178-58.44 E |
| 2 | 31 | 5521 | 9-30.38 N | 159-10.14 E |  | 1 | 66 | 5486 | 9-29.57 N | 178-47.96 E |
| 2 | 32 | 5520 | 9-31.15 N | 160-00.25 E |  |  |  |  |  |  |
| 2 | 33 | 5519 | 9-25.17 N | 160-50.30 E |  |  |  |  |  |  |
| 2 | 34 | 5518 | 9-29.53 N | 161-40.02 E |  |  |  |  |  |  |
| 2 | 35 | 5517 | 9-29.05 N | 162-29.27 E |  |  |  |  |  |  |

Table 3. Information of deployed float.

| Float | Date and Time | Position of deployment | PI |  |
| --- | --- | --- | --- | --- |
| WMO number | of deployment (UTC) | Latitude | Longitude |  |  |
| 5904990 | 2015 July 28 10:59 | 20-23.55 N | 156-44.18 E | JAMSTEC | ARVOR |
| 2902959 | 2015 Sep. 9 02:00 | 24-58.68 N | 138-42.79 E | JMA | APEX |

ARVOR: nke Instrumentation (France)

APEX: Teledyne Webb Research (USA)

List of Principal Investigators for all Measurements

The principal investigator (PI) and the person in charge responsible for major parameters measured on the cruise are listed in Table 4.

Table 4. List of principal investigator and the person in charge on the ship for RF15-07.

Item			Principal Investigator（PI）	Person in charge on the ship

Hydrography

CTDO2 / LADCP	Toshiya NAKANO			Nobumi KATO

Salinity 		Toshiya NAKANO			Koichi WADA

Dissolve oxygen		Toshiya NAKANO			Chihiro KAWAMURA

Nutrients		Toshiya NAKANO			Takahiro KITAGAWA

Phytopigment		Toshiya NAKANO			Takahiro KITAGAWA

DIC			Toshiya NAKANO			Shu SAITO

Total Alkalinity		Toshiya NAKANO			Shu SAITO

pH			Toshiya NAKANO			Shu SAITO

CFCs			Toshiya NAKANO			Kazutaka ENYO

Underway

Meteorology		Toshiya NAKANO			Keizo SHUTTA

Thermo-Salinograph	Toshiya NAKANO			Shu SAITO

pCO2			Toshiya NAKANO			Shu SAITO

Chlorophyll-a		Toshiya NAKANO			Takahiro KITAGAWA

ADCP			Toshiya NAKANO			Nobumi KATO

Bathymetry		Toshiya NAKANO			Nobumi KATO

Floats

Argo float (JMA)	Kazuhiro NEMOTO			Keizo SHUTTA

Argo float (JAMSTEC)	Shigeki HOSODA			Keizo SHUTTA

Toshiya NAKANO (nakano_t@met.kishou.go.jp)

Marine Division, Global Environment and Marine Department, JMA

1-3-4, Otemachi, Chiyoda-ku, Tokyo 100-8122, JAPAN

Phone: +81-3-3212-8341 Ext. 5131

Kazuhiro NEMOTO (k-nemoto@met.kishou.go.jp)

Marine Division, Global Environment and Marine Department, JMA

1-3-4, Otemachi, Chiyoda-ku, Tokyo 100-8122, JAPAN

Phone: +81-3-3212-8341 Ext. 5128

Shigeki HOSODA (hosodas@jamstec.go.jp)

Ocean Circulation Research Group,

Research and Development Center for Global Change (RCGC),

Strategic Research and Development area,

Japan Agency for Marine-Earth Science and Technology (JAMSTEC)

2-15 Natsushima, Yokosuka-shi, Kanagawa 237-0061, JAPAN

Reference

Swift, J. H. (2010): Reference-quality water sample data: Notes on acquisition, record keeping, and evaluation. IOCCP Report No.14, ICPO Pub. 134, 2010 ver.1